H/W concept

1) Handling PCB:

https://diyhacking.com/pcb-basics-tutorial/

2) ESD
eloctrostatic discharge.
https://www.slideshare.net/TransformingTech/electro-static-discharge-basics
3) Power Supply Selection
The use of power supplies for industrial and control applications requires careful consideration of the operating conditions, environment, and power loads. Here is a listing of some frequently overlooked considerations when selecting ac-dc power supplies.
## Hours of operation
Sometimes a low-cost power supply is selected for applications that require 24/7 operation. This is penny-wise and pound-foolish since the construction of low-cost supplies employs low-cost components (capacitors, active components, fans, etc.) that are unsuited for constant operation. The best solution for 24/7 applications is to find an industrial-rated power supply that includes a 5-year or longer warranty. The "warranty period" is a good indication of the type of components used in powersupply construction.
## Peak power loads
Many times industrial and control equipment includes dc motors, solenoids, pumps, etc. These types of loads typically have a peak start-up current that exceeds their steady state current. The system designer can either select a power supply that handles the peak current or consider a lower cost solution by employing a peak-rated power supply.
## Ambient temperatures
One of the biggest killers of power supplies is heat. Since all power supplies generate heat due to their inherent inefficiencies, they require cooling by conduction via heat sinks, natural air convection, forced air-cooling, or a combination of all three. However, whichever cooling method is employed, due consideration to the prevailing ambient air temperature range must be included in the end equipment design.
## Corrosive or dusty environments
When fan-cooled power supplies are employed in corrosive or dusty environments, a scheduled maintenance program must be established to periodically clean air filters and replace fans because their bearings will wear out quickly under these conditions. In these environments, it would be wise to consider non-fan cooled power supplies that are cooled via conduction or natural airflow (without fans).
## AC line noise
Most ac-dc power supplies include electromagnetic (EMI) filters. These embedded EMI filters serve to protect the ac line from noise generated by the supply as well as to protect the supply from noise generated by other devices connected to the ac line
4) Using Lab Equipment
### Multimeter
A multimeter's measurement flexibility combined with their precision and accuracy make multimeters an essential tool in any electronics lab.
Multimeters will typically be able to measure both AC and DC voltage and current as well as resistance. Multimeters are often used in troubleshooting designs and testing prototype circuits. Multimeter accessories include transistor testing modules, temperature sensor probes, high voltage probes, and probe kits. Multimeters are available for as little as $10 and can run several thousand for a high accuracy, high precision benchtop unit.
### LCR Meter
As versatile as multimeters are, they cannot measure capacitance or inductance which is where the LCR meter (Inductance (L), Capacitance (C), and Resistance (R)) comes into the picture. LCR meters come in two variants, a lower cost version that measures the total impedance of a component and a more expensive type that measures all of the components of the impendence of the component, equivalent series resistance (ESR) and the Quality (Q) factor of the component.
The accuracy of low-cost LCR meters is often quite poor, with tolerances as high as 20%. Since many capacitors have a 20% tolerance themselves, compounding the tolerance of the meter and component can cause additional problems in designing and troubleshooting electronics.
### Oscilloscope
Electronics are all about the signals and the oscilloscope is the primary measurement tool to observe the shape of signals.
Oscilloscopes, often called oscopes or just scopes, display signals in a graphical format on a pair of axes, generally with Y as the voltage and X as the time. This is a very powerful way to quickly see the shape of a signal, determine what is going on in an electronic circuit and monitor performance or track down problems. Oscilloscopes are available in digital and analog variants, starting at a few hundred dollars and running into the tens of thousands for the top of the line models. Digital scopes have several measurements and trigger options built into the system which make measurements of peak-to-peak voltage, frequency, pulse width, rise time, signal comparisons, and recording waveforms simple tasks.
### Soldering Iron
The core tool for assembling electronics is the soldering iron, a hand tool used to melt solder to form an electrical and physical connection between two surfaces. Soldering irons come in a few forms, with the cheapest being plugged directly into an outlet from the hand tool. While these soldering irons work, for most electronics work a temperature controlled soldering station is much preferred. The tip of a soldering iron is heated by a resistive heater and often monitored by a temperature sensor to keep the temperature of the tip steady.
Soldering iron tips are often removable and are available in a range of shapes and styles to accommodate different types of soldering work.
### Precision Mechanical Tools
Every electronics labs needs a few key mechanical hand tools to help with the basic tasks and make the more complex tasks much easier. Some of the key tools include shear cutters, wire strippers, ESD-safe tweezers, needle nose pliers, precision screwdriver set, "third hand" tools, and alligator/test clips and leads. Some tools, such as the ESD safe tweezers, are essential for surface mount work while other tools, such as the "third hand" tool are very useful when soldering components to a PCB and the component, PCB, soldering iron and solder all need to be held in place.
### Optics
Electronic components get very very small. Small enough that they can be difficult to hold with even precision tweezers let alone see. Basic lab optics such as a magnifying loupes and large articulated magnifying lenses are useful in many cases, but do not provide a great deal of magnification, with 5-10x magnification available at the higher end. Loupes and magnifying lenses work well for basic lab needs, but if surface mount assembly and inspection work will be done, then a stereomicroscope is ideal. For surface mount work, a stereomicroscope that provides between 25x and +90x magnification which supports precision soldering of surface mount chips and board level inspection. Stereomicroscopes start at around $500 and are available in fixed or variable zoom, multiple lighting options, and additional optical paths for mounting cameras or for multiple users.
### Power Supply
In the end, it's difficult to test a circuit without applying power to it. Several types of power supplies are available to support electronics design and testing with a number of features. For a general purpose laboratory power supply, variable voltage and current controls are one of the most important features. This allows one supply to provide a wide range of voltages that can be adjusted for any application. Often these power supplies can operate in either a constant voltage or constant current mode, allowing rapid testing of components or portions of a design without building a specific power regulation circuit.
### Other Equipment
The equipment above only scratches the surface of the equipment that is available and might be critical for your application. Some of the other common equipment with more of a focused use includes:
- Function Generators
- Signal Generators
- Spectrum Analyzers
- Signal Analyzers
- Pattern Generator
- Protocol Analyzer
- Network Analyzer
- Transistor Tester
5) Clock & Reset
RESET is an active High input When RESET is set to High, 8051 goes back to the power on state.The 8051 is reset by holding the RST high for at least two machine cycles and then returning it low.

There are two method of reset circuit:
1.Power On Reset.
- Initially charging of capacitor makes RST High
- When capacitor charges fully it blocks DC.
2.Manual Reset
closing the switch momentarily will make RST High.

After a reset, the program counter is loaded with 0000H but the content of on-chip RAM is not affected.

6) Pin Strapping.

To assign a default state of a pin on power on or reset time.
When do we use : If a logic value '0' or '1' is an active value of this pin, and you don't want to be activated it on power-on or reset,
you may strap it to a value that you need...

7) JTAG
http://www.embedded.com/electronics-blogs/beginner-s-corner/4024466/Introduction-to-JTAG
The specification JTAG devised uses boundary-scan technology, which enables engineers to perform extensive debugging and diagnostics on a system through a small number of dedicated test pins. Signals are scanned into and out of the I/O cells of a device serially to control its inputs and test the outputs under various conditions. Today, boundary-scan technology is probably the most popular and widely used design-for-test technique in the industry.

Test pins
Devices communicate to the world via a set of I/O pins. By themselves, these pins provide limited visibility into the workings of the device. However, devices that support boundary scan contain a shift-register cell for each signal pin of the device. These registers are connected in a dedicated path around the device's boundary (hence the name), as shown in Figure 1. The path creates a virtual access capability that circumvents the normal inputs and provides direct control of the device and detailed visibility at its outputs.

Figure 1: An integrated circuit with boundary scan
During testing, I/O signals enter and leave the chip through the boundary-scan cells. The boundary-scan cells can be configured to support external testing for interconnection between chips or internal testing for logic within the chip.
To provide the boundary scan capability, IC vendors add additional logic to each of their devices, including scan registers for each of the signal pins, a dedicated scan path connecting these registers, four or five additional pins, and control circuitry. The overhead for this additional logic is minimal and generally well worth the price to have efficient testing at the board level.