Device Drivers

### Listing Loaded Modules With lsmod
In order to see the list of currently loaded Modules, use the lsmod command
$/sbin/lsmod

### The /lib/modules Directory
- Contains the Modules for the different Kernel versions we have installed.
- One directory per Kernel, named after the Kernel's version number.
- Modules are split into directories, based on categories:
  - pcmcia - PCMCIA Drivers, for laptops.
  - kernel/net - network-related Modules (firewall, extra protocols support, etc.)
  - kernel/drivers - Drivers for various types of Hardware (including network Drivers).
  - kernel/fs - file-systems support (ext3, vfat, etc.)
  - kernel/arch - Architecture-specific support (e.g. Drivers to handle features of a a specific CPU or motherboard).
## Loading And Unloading Kernel Modules - insmod/rmmod
- Module loading and unloading may only be performed by root.
- To load a Kernel Module, use the insmod command:
  [root@simey ~]# insmod eeprom
Check with lsmod that the Module was indeed loaded.
To un-load a Kernel Module, use the rmmod command:
[root@simey ~]# rmmod eeprom

Check with lsmod that the Module was indeed un-loaded.
### Handling Kernel Module Dependencies - depmod and modprobe
- Modules could depend on each other. For example, to load the Module 'lm78', we need to first load 'i2c-core' and 'i2c-proc'.
- The depmod command builds a list of Module dependencies - i.e. for each Module, which other Modules it needs, in order to load. Run it as:
  [root@simey ~]# depmod -a
In order to have the system take care of these loading dependencies automatically, load a Module using the modprobe command:
[root@simey ~]# modprobe lm78

[root@simey ~]# modprobe -v lm78
### The /etc/modules.conf file
- Contains 'default' parameters for Modules we use often (e.g. network Drivers, sound cards, etc.)
- commonly used lines:
  - alias - specifies that a given Module (Driver) should be used for a given Hardware Device. example:
    alias eth0 8139too
  - options - specifies options to supply to a given Module, when it is loaded. example:
    options sb io=0x220 irq=5 dma=1 dma16=0 mpu_io=0x310
- Note: module options may also be supplied as parameters to the insmod and modprobe commands.
### Getting Information About A Kernel Module - modinfo
- In order to get information about a Module (author, supported options), we may use the modinfo command.
- For example, information about the 'mousedev' Module:
  [choo@simey ~]$ /sbin/modinfo mousedev

### Programming of Device driver

https://www.youtube.com/watch?v=Zn8mEZXr6nE
- vi ex01_simple_module.c

#include <linux/init.h>
#include <linux/module.h>

/* start function */
int __init ex01_simple_module_init(void)
{
    printk(KERN_ALERT "Inside the %s function\n", __FUNCTION__);
    return 0;
}

/* end function (we can put any name to exit function) */
void __exit ex01_simple_module_exit(void)
{
    printk(KERN_ALERT "Inside the %s function\n", __FUNCTION__);
}

/* macros calling of function */
module_init(ex01_simple_module_init);
module_exit(ex01_simple_module_exit);
vvdn@vvdn:~/Mayur_shankariya/Training

----------------------------------------------------------------------------­ --------
---> We need to know kernal version
$uname -r

--->creat one makefile to build kernal object file

$vi Makefile
/* obj-m to generate kernal object file it give object file as same name of this .o file.
obj-m := ex01_simple_module.o

--->to run make command
$ make -C /lib/modules/$(uname -r)/build M=$PWD modules

--->to insert the module into kernal space
$sudo insmod ./ex01_simple_module.ko

--->to show the execution of file
$ls /var/log/syslog
$sudo tail -f /var/log/syslog

--->then open new terminal same pwd
$sudo insmod ./ ex01_simple_module.ko
$sudo rmmod ./ ex01_simple_module.ko

---> to add other module into kernal
$vi Makefile
/* ‘:’ it use basically initializaton to obj-m and ‘+=’ is used for add new modules. */
obj-m := ex01_simple_module.o
obj-m += ex02_simple_module_init.o
obj-m += ex03_simple_module_exit.o

# Linux Device Drivers Modules from Multiple C Files, MODULE_LICENSE(), __init
Changes only in makefile whatever had previose section.

$vi Makefile
  obj-m := ex01_simple_module.o
  obj-m += ex02_simple_module_init.o
  obj-m += ex03_simple_module_exit.o

  obj-m := ex0203_simple_module.o
        ex0203_simple_module-objs := ex02_simple_module_init.o ex03_simple_module_exit.o

$!make
$sudo tail -f /var/log/syslog
another terminal
$sudo insmod ./ex0203_simple_module.ko
$sudo rmmod ./ex0203_simple_module.ko

# Linux Device Drivers Exporting Symbols

$vi ex04_exporting_symbol.c

 #include <linux/init.h>
 #include <linux/module.h>

 int ex04_simple_module_function(void)
 {
    printk(KERN_ALERT "Inside the %s function\n", __FUNCTION__);
    return 0;
 }

 EXPORT_SYMBOL(ex04_simple_module_function);

 int __init ex04_simple_module_init(void)
 {
      printk(KERN_ALERT "Inside the %s function\n", __FUNCTION__);
      return 0;
  }

  /* end function (we can put any name to exit function) */
  void __exit ex04_simple_module_exit(void)
  {
      printk(KERN_ALERT "Inside the %s function\n", __FUNCTION__);
  }

  /* macros calling of function */
  module_init(ex04_simple_module_init);
  module_exit(ex04_simple_module_exit);

$vi ex04_using_symbol.c

#include <linux/init.h>
#include <linux/module.h>

int ex04_simple_module_function(void);

int ex04_simple_module_init(void)
{
    printk(KERN_ALERT "Inside the %s function\n", __FUNCTION__);
    ex04_simple_module_function();

    return 0;
}

void ex04_simple_module_exit(void)
{
    printk(KERN_ALERT "Inside the %s function\n", __FUNCTION__);
}

module_init(ex04_simple_module_init);
module_exit(ex04_simple_module_exit);

$vi Makefile
obj-m := ex01_simple_module.o
obj-m += ex02_simple_module_init.o
obj-m += ex03_simple_module_exit.o

#to add multiple .o file
obj-m := ex0203_simple_module.o
        ex0203_simple_module-objs := ex02_simple_module_init.o ex03_simple_module_exit.o

obj-m := ex04_exporting_symbol.o
obj-m += ex04_using_symbol.o

$make -C /lib/modules/$(uname -r)/build M=$PWD clean
$make -C /lib/modules/$(uname -r)/build M=$PWD modules
$!make
$sudo tail -f var/log/syslogWrite an advanced Makefile which includes all the above concepts for
Employee database program (codebase should be as like project directory
structure)
another terminal
$sudo insmod ./ex04_exporting_symbol.c
$sudo insmod ./ex04_using_symbol.c
$sudo rmmod ./ex04_exporting_symbol.c

# Linux Device Drivers Simple Character Driver
https://www.youtube.com/watch?v=E_xrzGlHbac

$vi ex07_simple_char_drv.c
/* to show file_operations structure */
$vim /lib/modules/$(uname -r)/ build/include/linux/fs.h
$vi Makefile
obj-m := ex07_simple_char_drv.o

$ make -C /lib/modules/$(uname -r)/build M=$PWD modules
to show our driver
$ cat /proc/devices
to change permission
$sudo mknod -m 666 /dev/simple_char_device c 240 0
to show permission has changed or not
$ls -l /dev/simple_char_device
$sudo tail -f /var/log/syslog
another terminal
$ cat /dev/simple_char_device
$echo “testing” > /dev/simple_char_device

 DYNAMIC MEMORY ALLOCATION TO KERNEL

http://www.roman10.net/2011/07/29/linux-kernel-programmingmemory-allocation/

There’re two functions available to allocate memory from heap in Linux kernel process,
1. vmalloc
The vmalloc function is defined in /lib/modules/$(uname -r)/build/include/linux/vmalloc.h as below,
void *vmalloc(unsigned long size);
It’s Linux kernel’s version of malloc() function, which is used in user space. Like malloc, the function allocates virtually contiguous memory that may or may not physically contiguous.
To free the memory space allocated by vmalloc, one simply call vfree(), which is defined as,
void vfree(const void *addr);
2. kmalloc
The most commonly used memory allocation function in kernel is kmalloc, which is defined in /lib/modules/$(uname -r)/build/include/linux/slab.h as below,
void * kmalloc(size_t size, int flags);
kmalloc allocates a region of physically contiguous (also virtually contiguous) memory and return the pointer to the allocated memory. It returns NULL when the operation fails.
The behavior of kmalloc is dependent on the second parameter flags. Here only the two most popular flags are introduced,
GFP_KERNEL: this flag indicates a normal kernel memory allocation. The kernel might block the requesting code, free up enough memory and then continue the allocation. It cannot be used in places where sleep is not allowed.
GFP_ATOMIC: this flag indicates the kmalloc function is atomic operation. Atomic operation means the function is performed entirely or not performed at all. It cannot block at the middle of execution. As the kernel cannot jump out of the allocation and free up memory to satisfy the function request, this function has a higher chance of failure with this flag passed in.
There’re several other flags, for example, GFP_DMA for allocation of memory space capable of undergoing Direct Memory Access. For more information, one can refer the links provided in the references section.
To free up the memory allocated by kmalloc, one can use kfree defined as below,
void kfree(const void *objp);
3. vmalloc VS kmalloc
vmalloc allocates virtually contiguous memory space (not necessarily physically contiguous), while kmalloc allocates physically contiguous memory (also virtually contiguous). Most of the memory allocations in Linux kernel are done using kmalloc, due to the following reasons:
- On many architectures, hardware devices don’t understand virtual address. Therefore, their device drivers can only allocate memory using kmalloc.
- kmalloc has better performance in most cases because physically contiguous memory region is more efficient than virtually contiguous memory. The reason behind this is not covered here, interested readers can search for Linux memory management articles.
But when a large chunk of memory is needed, vmalloc is used often as it doesn’t require physically contiguous memory and the kernel can satisfy the request with much less effort than using kmalloc.

seq_file interface

The seq_file interface

        Copyright 2003 Jonathan Corbet <corbet@lwn.net>
        This file is originally from the LWN.net Driver Porting series at
        http://lwn.net/Articles/driver-porting/

There are numerous ways for a device driver (or other kernel component) to
provide information to the user or system administrator. One useful
technique is the creation of virtual files, in debugfs, /proc or elsewhere.
Virtual files can provide human-readable output that is easy to get at
without any special utility programs; they can also make life easier for
script writers. It is not surprising that the use of virtual files has
grown over the years.

Creating those files correctly has always been a bit of a challenge,
however. It is not that hard to make a virtual file which returns a
string. But life gets trickier if the output is long - anything greater
than an application is likely to read in a single operation. Handling
multiple reads (and seeks) requires careful attention to the reader's
position within the virtual file - that position is, likely as not, in the
middle of a line of output. The kernel has traditionally had a number of
implementations that got this wrong.

The 2.6 kernel contains a set of functions (implemented by Alexander Viro)
which are designed to make it easy for virtual file creators to get it
right.

The seq_file interface is available via <linux/seq_file.h>. There are
three aspects to seq_file:

     * An iterator interface which lets a virtual file implementation
       step through the objects it is presenting.

     * Some utility functions for formatting objects for output without
       needing to worry about things like output buffers.

     * A set of canned file_operations which implement most operations on
       the virtual file.

We'll look at the seq_file interface via an extremely simple example: a
loadable module which creates a file called /proc/sequence. The file, when
read, simply produces a set of increasing integer values, one per line. The
sequence will continue until the user loses patience and finds something
better to do. The file is seekable, in that one can do something like the
following:

    dd if=/proc/sequence of=out1 count=1
    dd if=/proc/sequence skip=1 of=out2 count=1

Then concatenate the output files out1 and out2 and get the right
result. Yes, it is a thoroughly useless module, but the point is to show
how the mechanism works without getting lost in other details. (Those
wanting to see the full source for this module can find it at
http://lwn.net/Articles/22359/).

Deprecated create_proc_entry

Note that the above article uses create_proc_entry which was removed in
kernel 3.10. Current versions require the following update

- entry = create_proc_entry("sequence", 0, NULL);
- if (entry)
- entry->proc_fops = &ct_file_ops;
+ entry = proc_create("sequence", 0, NULL, &ct_file_ops);

The iterator interface

Modules implementing a virtual file with seq_file must implement a simple
iterator object that allows stepping through the data of interest.
Iterators must be able to move to a specific position - like the file they
implement - but the interpretation of that position is up to the iterator
itself. A seq_file implementation that is formatting firewall rules, for
example, could interpret position N as the Nth rule in the chain.
Positioning can thus be done in whatever way makes the most sense for the
generator of the data, which need not be aware of how a position translates
to an offset in the virtual file. The one obvious exception is that a
position of zero should indicate the beginning of the file.

The /proc/sequence iterator just uses the count of the next number it
will output as its position.

Four functions must be implemented to make the iterator work. The first,
called start() takes a position as an argument and returns an iterator
which will start reading at that position. For our simple sequence example,
the start() function looks like:

        static void *ct_seq_start(struct seq_file *s, loff_t *pos)
        {
        loff_t *spos = kmalloc(sizeof(loff_t), GFP_KERNEL);
        if (! spos)
        return NULL;
        *spos = *pos;
        return spos;
        }

The entire data structure for this iterator is a single loff_t value
holding the current position. There is no upper bound for the sequence
iterator, but that will not be the case for most other seq_file
implementations; in most cases the start() function should check for a
"past end of file" condition and return NULL if need be.

For more complicated applications, the private field of the seq_file
structure can be used. There is also a special value which can be returned
by the start() function called SEQ_START_TOKEN; it can be used if you wish
to instruct your show() function (described below) to print a header at the
top of the output. SEQ_START_TOKEN should only be used if the offset is
zero, however.

The next function to implement is called, amazingly, next(); its job is to
move the iterator forward to the next position in the sequence. The
example module can simply increment the position by one; more useful
modules will do what is needed to step through some data structure. The
next() function returns a new iterator, or NULL if the sequence is
complete. Here's the example version:

        static void *ct_seq_next(struct seq_file *s, void *v, loff_t *pos)
        {
        loff_t *spos = v;
        *pos = ++*spos;
        return spos;
        }

The stop() function is called when iteration is complete; its job, of
course, is to clean up. If dynamic memory is allocated for the iterator,
stop() is the place to free it.

        static void ct_seq_stop(struct seq_file *s, void *v)
        {
        kfree(v);
        }

Finally, the show() function should format the object currently pointed to
by the iterator for output. The example module's show() function is:

        static int ct_seq_show(struct seq_file *s, void *v)
        {
        loff_t *spos = v;
        seq_printf(s, "%lld\n", (long long)*spos);
        return 0;
        }

If all is well, the show() function should return zero. A negative error
code in the usual manner indicates that something went wrong; it will be
passed back to user space. This function can also return SEQ_SKIP, which
causes the current item to be skipped; if the show() function has already
generated output before returning SEQ_SKIP, that output will be dropped.

We will look at seq_printf() in a moment. But first, the definition of the
seq_file iterator is finished by creating a seq_operations structure with
the four functions we have just defined:

        static const struct seq_operations ct_seq_ops = {
        .start = ct_seq_start,
        .next = ct_seq_next,
        .stop = ct_seq_stop,
        .show = ct_seq_show
        };

This structure will be needed to tie our iterator to the /proc file in
a little bit.

It's worth noting that the iterator value returned by start() and
manipulated by the other functions is considered to be completely opaque by
the seq_file code. It can thus be anything that is useful in stepping
through the data to be output. Counters can be useful, but it could also be
a direct pointer into an array or linked list. Anything goes, as long as
the programmer is aware that things can happen between calls to the
iterator function. However, the seq_file code (by design) will not sleep
between the calls to start() and stop(), so holding a lock during that time
is a reasonable thing to do. The seq_file code will also avoid taking any
other locks while the iterator is active.

Formatted output

The seq_file code manages positioning within the output created by the
iterator and getting it into the user's buffer. But, for that to work, that
output must be passed to the seq_file code. Some utility functions have
been defined which make this task easy.

Most code will simply use seq_printf(), which works pretty much like
printk(), but which requires the seq_file pointer as an argument.

For straight character output, the following functions may be used:

        seq_putc(struct seq_file *m, char c);
        seq_puts(struct seq_file *m, const char *s);
        seq_escape(struct seq_file *m, const char *s, const char *esc);

The first two output a single character and a string, just like one would
expect. seq_escape() is like seq_puts(), except that any character in s
which is in the string esc will be represented in octal form in the output.

There are also a pair of functions for printing filenames:

        int seq_path(struct seq_file *m, const struct path *path,
        const char *esc);
        int seq_path_root(struct seq_file *m, const struct path *path,
        const struct path *root, const char *esc)

Here, path indicates the file of interest, and esc is a set of characters
which should be escaped in the output. A call to seq_path() will output
the path relative to the current process's filesystem root. If a different
root is desired, it can be used with seq_path_root(). If it turns out that
path cannot be reached from root, seq_path_root() returns SEQ_SKIP.

A function producing complicated output may want to check
        bool seq_has_overflowed(struct seq_file *m);
and avoid further seq_<output> calls if true is returned.

A true return from seq_has_overflowed means that the seq_file buffer will
be discarded and the seq_show function will attempt to allocate a larger
buffer and retry printing.

Making it all work

So far, we have a nice set of functions which can produce output within the
seq_file system, but we have not yet turned them into a file that a user
can see. Creating a file within the kernel requires, of course, the
creation of a set of file_operations which implement the operations on that
file. The seq_file interface provides a set of canned operations which do
most of the work. The virtual file author still must implement the open()
method, however, to hook everything up. The open function is often a single
line, as in the example module:

        static int ct_open(struct inode *inode, struct file *file)
        {
        return seq_open(file, &ct_seq_ops);
        }

Here, the call to seq_open() takes the seq_operations structure we created
before, and gets set up to iterate through the virtual file.

On a successful open, seq_open() stores the struct seq_file pointer in
file->private_data. If you have an application where the same iterator can
be used for more than one file, you can store an arbitrary pointer in the
private field of the seq_file structure; that value can then be retrieved
by the iterator functions.

There is also a wrapper function to seq_open() called seq_open_private(). It
kmallocs a zero filled block of memory and stores a pointer to it in the
private field of the seq_file structure, returning 0 on success. The
block size is specified in a third parameter to the function, e.g.:

        static int ct_open(struct inode *inode, struct file *file)
        {
        return seq_open_private(file, &ct_seq_ops,
        sizeof(struct mystruct));
        }

There is also a variant function, __seq_open_private(), which is functionally
identical except that, if successful, it returns the pointer to the allocated
memory block, allowing further initialisation e.g.:

        static int ct_open(struct inode *inode, struct file *file)
        {
        struct mystruct *p =
        __seq_open_private(file, &ct_seq_ops, sizeof(*p));

        if (!p)
        return -ENOMEM;

        p->foo = bar; /* initialize my stuff */
        ...
        p->baz = true;

        return 0;
        }

A corresponding close function, seq_release_private() is available which
frees the memory allocated in the corresponding open.

The other operations of interest - read(), llseek(), and release() - are
all implemented by the seq_file code itself. So a virtual file's
file_operations structure will look like:

        static const struct file_operations ct_file_ops = {
        .owner = THIS_MODULE,
        .open = ct_open,
        .read = seq_read,
        .llseek = seq_lseek,
        .release = seq_release
        };

There is also a seq_release_private() which passes the contents of the
seq_file private field to kfree() before releasing the structure.

The final step is the creation of the /proc file itself. In the example
code, that is done in the initialization code in the usual way:

        static int ct_init(void)
        {
        struct proc_dir_entry *entry;

        proc_create("sequence", 0, NULL, &ct_file_ops);
        return 0;
        }

        module_init(ct_init);

And that is pretty much it.

seq_list

If your file will be iterating through a linked list, you may find these
routines useful:

        struct list_head *seq_list_start(struct list_head *head,
        loff_t pos);
        struct list_head *seq_list_start_head(struct list_head *head,
        loff_t pos);
        struct list_head *seq_list_next(void *v, struct list_head *head,
        loff_t *ppos);

These helpers will interpret pos as a position within the list and iterate
accordingly. Your start() and next() functions need only invoke the
seq_list_* helpers with a pointer to the appropriate list_head structure.

The extra-simple version

For extremely simple virtual files, there is an even easier interface. A
module can define only the show() function, which should create all the
output that the virtual file will contain. The file's open() method then
calls:

        int single_open(struct file *file,
        int (*show)(struct seq_file *m, void *p),
        void *data);

When output time comes, the show() function will be called once. The data
value given to single_open() can be found in the private field of the
seq_file structure. When using single_open(), the programmer should use
single_release() instead of seq_release() in the file_operations structure
to avoid a memory leak.

### Creation of proc entry using proc_create_data in kernel version 3.10 and above.

http://tuxthink.blogspot.in/2013/10/creation-of-proc-entrt-using.html

In the post "Creating read only proc entry in kernel versions above 3.10. " we saw how to create a proc entry using the function proc_create.
Note: The following module is valid only of kernel version 3.10 and above.
Another function available in kernel version 3.10 and above for creation of proc entry is proc_create_data which is defined in proc_fs.hs as

 struct proc_dir_entry *proc_create_data(const char *name, umode_t mode,struct proc_dir_entry *parent,const struct file_operations *proc_fops,void *data);

Where
name: The name of the proc entry
mode: The access mode for proc entry
parent: The name of the parent directory under /proc
proc_fops: The structure in which the file operations for the proc entry will be created.
data: If any data needs to be passed to the proc entry.
For example to create a proc entry by the name "hello" under /proc the above functions will be defined are

proc=proc_create_data("hello",0,NULL,&proc_fops,msg);

Along with creation of the entry we are also passing a function to the proc entry in using the porinter "msg".
Now we need to create file_operations structure proc_fops in which we can map the read function for the proc entry.

struct file_operations proc_fops = {
read: read_proc
};

Next we need to add the function read_proc which will give to the user space the data that we want to export from the kernel space.

int read_proc(struct file *filp,char *buf,size_t count,loff_t *offp )
{
char *data;
data=PDE_DATA(file_inode(filp));
if(!(data)){
printk(KERN_INFO "Null data");
return 0;
}

if(count>temp)
{
count=temp;
}
temp=temp-count;

copy_to_user(buf,data, count);
if(count==0)
temp=len;
return count;
}

To access the data in the proc_dir_structure we need to make use of the function PDE_DATA to which we pass the file pointer. The function in turn returs a pointer to the data that was passed during the creation of the proc entry.
The message that we want to display will be defined in the function create_new_proc_entry in which we will also call the fuction for creation of proc entry.

void create_new_proc_entry()
{

msg="Hello World ";
proc=proc_create_data("hello",0,NULL,&proc_fops,msg);

len=strlen(msg);
temp=len;

}

The init and clean up functions for the module are

int proc_init (void) {
        create_new_proc_entry();
        return 0;
}

void proc_cleanup(void) {
        remove_proc_entry("hello",NULL);
}

The full code for creation of proc entry using proc_create_data is
proc_read_data.c

#include <linux/module.h>
#include <linux/kernel.h>
#include <linux/proc_fs.h>
#include <linux/sched.h>
#include <linux/mm.h>
#include <linux/slab.h>
#include <asm/uaccess.h>
#include <asm/types.h>

struct proc_dir_entry *proc;
int len,temp;
char *msg;

int read_proc(struct file *filp,char *buf,size_t count,loff_t *offp )
{
char *data;
data=PDE_DATA(file_inode(filp));
if(!(data)){
printk(KERN_INFO "Null data");
return 0;
}

if(count>temp)
{
count=temp;
}
temp=temp-count;

copy_to_user(buf,data, count);
if(count==0)
temp=len;
return count;
}

struct file_operations proc_fops = {
read: read_proc
};

void create_new_proc_entry()
{

msg="Hello World ";
proc=proc_create_data("hello",0,NULL,&proc_fops,msg);

len=strlen(msg);
temp=len;
}

int proc_init (void) {
 create_new_proc_entry();
 return 0;
}

void proc_cleanup(void) {
 remove_proc_entry("hello",NULL);
}

MODULE_LICENSE("GPL");
module_init(proc_init);
module_exit(proc_cleanup);

The makefile for the compilation of the modules are

ifneq ($(KERNELRELEASE),)
   obj-m := proc_read_data_3_10.o
else

#KERNELDIR ?= /lib/modules/$(shell uname -r)/build
KERNELDIR ?= /home/nitin/Desktop/src/linux-3.11.1/

PWD := $(shell pwd)

default:
        $(MAKE) -C $(KERNELDIR) M=$(PWD) modules
endif
clean:
        $(MAKE) -C $(KERNELDIR) M=$(PWD) clean

Compile and load the module using

$ make
$ sudo insmod proc_read_3_10.ko

We can see the output by using the cat command

$ cat /proc/hello
Hello World